# Ridiculous Speed

Rocket by: David Raimondi

Length 7 feet, 1 inch tall

Weight without motor: 3.19 lbs

Weight with motor:    10.25 lbs

Electronics: GWiz MC

Parachutes:    12” Drogue

48” Main

Motor by: James Marino

EX L1771 Wimpy Red

Length: 35.5”

Propellant length: 32”

Rocket was MIA for 6 days before

it was found by Cindy Carter.

Flight statistics:

Recorded Altitude: 21,624 ft.

Max Speed: Mach 2+

Rocket Crew: David Raimondi,

James Marino

Lift-off photo: altitude ~50 ft. , speed ~500 ft./sec.